## Slide 1
Open-Source Grid2Demand:
A tool for generating zone-to-zone travel demand based on grid zones
  Mini-lessions through teaching dialog
  Sevgi Erdogan,
  Anjun Li,
  Taehooie Kim,
  Xuesong (Simon) Zhou

## Slide 2: Inclusive Excellence
https://inclusion.asu.edu/

## Slide 3: Part 1 Introduction to DTALite/NeXTA
1.1 Project Objective and Motivations
1.2 What NeXTA/DTALite Can Do
1.3 Open-source Free Software Package

## Slide 4: Motivations
Adopting open network standard of GMNS
General Travel Network Format Specification is a product of Zephyr Foundation, which aims to advance the field through flexible and efficient support, education, guidance, encouragement, and incubation. Further details can be found in https://zephyrtransport.org/projects/2-network-standard-and-tools/
Integrated graphic user interface and analysis package
(1) Provide an open-source code base to enable transportation researchers and software developers to expand its range of capabilities to various traffic management application.
(2) Present results to other users by visualizing time-varying traffic flow dynamics and traveler route choice behavior in an integrated environment.
(3) Provide a free, educational tool for students to understand the complex decision-making process in transportation planning and optimization processes.

## Slide 5: Motivations (II)
  Existing technical barriers: (based on DTA user survey, TRB network modeling committee, 2009)
    Require too many input data: 47%
    Take too long to run: 35%
    Model is unclear: 35%
    Our goals
    Simplified data input from static traffic assignment
    Use parallel computing capability, simplified routing and simulation
    Open-source
Visualization: Seeing is believing
Excel Tools: Start from basics

## Slide 6: What DTALite/NeXTA Can Do
Open-source traffic simulation/modeling Data Hub
    Integrated simulated and measured data management tools
    Connection with Travel demand model, signal optimization tool (Synchro)
Large-scale dynamic traffic assignment
    Typical network size: 2K~5K zones, 20K~50K links, 2~4 Million vehicles
Network scenario analysis
    Rich outputs: various operational performance measures
    Road pricing application: Consider time-dependent toll, Heterogeneous Value of times

## Slide 7
Q-GIS/OSM Maps
Other Visualization
NeXTA
Large-scale Dynamic Traffic Assignment & Simulator
Corridor-level VOC contour
Simulation vs. Observation Comparison
Rich Output
What NeXTA/DTALite Can Do

## Slide 8
Field Data
Land Use, Safety & Emissions Models
HCM & Signal Timing Models
Micro-simulation Models
Dynamic Traffic Assignment Models
Travel Demand Forecasting Models
Data Hub
Field Data
Land Use, Safety & Emissions Models
HCM & Signal Timing Models
Micro-simulation Models
Dynamic Traffic Assignment Models
Travel Demand Forecasting Models
NeXTA Data Hub
Current Practice Ad Hoc
With NeXTA Data Hub Systematic
Integrated Modeling Practice
What NeXTA/DTALite Can Do

## Slide 9: Open-source Free Software Package
NEXTA: front-end GUI (C++)
  Version 0.5: GUI for TRANSIMS and DYNASMART
  Version 0.9: GNU Open-source data hub
    Import
      Other regional planning models (TransCAD, VISSUM, Cube)
      GIS shape files
      Traffic volume, speed, GPS data, Google Public Transit Feed
    Export
      QQ-GIS
      Prepare network and signal data
DTALite: Open-source computational engine (C++)
  Light-weight and agent-based DTA
  Built-in OD demand matrix estimation (ODME) program

## Slide 10: AMS Data Hub Software Prototype: NeXTA
Start with GIS with multiple transportation layers
  1. node,
  2. link,
  3. agent,
  4. trajectory,
  5. signal timing.
Focus on data processing and visualization

## Slide 11: Useful Materials
DTALite Software Release
  https://github.com/xzhou99/dtalite_software_release
DTALite White paper
  DTALite: A queue-based mesoscopic traffic simulator for fast model evaluation and calibration, by Zhou and Taylor, 2014
  https://www.tandfonline.com/doi/full/10.1080/23311916.2014.961345
DTALite Source Codes
  Python: https://github.com/asu-trans-ai-lab/DTALite
  C++: https://github.com/xzhou99/dtalite_beta_test

## Slide 12: Mesoscopic Traffic Simulation

## Slide 13: Computational Challenges
Maryland State-wide model:
20 K nodes, 47K links, 3,000 zones, 18 M agents
CPU time: 30 min per UE iteration on a 20-core workstation with 194 GB RAM
  Shared memory-based parallel computing for agent-based path finding and mesoscopic traffic simulation (based on OpenMP)

## Slide 14: Traffic Flow Theoretical Foundation: LWR Equations
Hyperbolic system of conservation laws
  where q, k are flow and density, respectively, and g(·) is the net vehicle generation rate.
Traffic flow model
  Speed (or flow) of traffic is a function of density only
  E.g. Greenshields model: V = Vfree (1 – k/Kjam)

## Slide 15: Numerical Calculation Scheme Based on Link Flow/Density (Used in CTM)
Notation
  Δt = length of simulation interval (e.g. 1 sec, 6 sec)
  Δx = cell length (e.g. 0.5 mile)
  ki,t , vi,t =the prevailing density and mean speed in cell i during the tth time step
  qi,t = transfer flow rate from section i to cell i+1 during the tth time interval [t, t+Δt].
Computation Procedure
  Step 1: Calculate prevailing speed vi,t according to a traffic flow model
  Step 2: Calculate flow ready to move from cell i-1 to section i: vi,tki,t
  Step 3: Calculate transfer flow from section i to cell i+1
qi,t = Min { vi,t  ki,t , qmax i+1,t }
  Step 4: Update prevailing density at cell i
ki,t+1 = ki,t + (qi-1,t – qi,t)  Δt /Δ x
Issue: transfer flow qi,t is an explicit function of the occupancy at the current cell, other than the downstream capacity
    Transferred flow exceeds the spatial storage capacity at the next cell

## Slide 16: Newell’s N-Curve Approach (Used in DTALite)
Ni (t): cumulative flow counts at location i at time t
  q=[Ni(t+1)-Ni(t)]/Δt
  K=[Ni+1(t)-Ni(t)]/ΔX
Focus on N-curve at transfer points
  N=Min {Nupstream, Ndownstream}
Focus on change of N along a characteristic line (wave) at sections
  dN = (N/x)dx + (D/t)dt = - kdx + qdt =
  (-k+ q  wave)dx
  if wave=vfree, dN=( -k + k) dx=0
  if wave=w, dN=-(k+qw)dx= -kjamdx

## Slide 17: Illustration of N-Curve Computation For Tracking Queue Spillback

## Slide 18: System Architecture and Data Flow
Data or progress | Corresponding functions or class
Link-Node Network Data | Class :Node(),Link() Functions: g_read_input_data()
Origin-destination Demand Profile | Class :Agent() Functions: g_read_input_data()
DTALite:Meso-scopic Dynamic Traffic Assignment and Spatial Queue-based Traffic Simulation | Class :Network() Functions: g_traffic_assignment() g_traffic_simulation()

## Slide 19: Simulation Logic as Simple Queue
Can be viewed as pseudo event-based simulation and we do not simulate how a vehicle moves inside the link
Vehicle is moved into an in-flow queue at time ta
Calculate time entering the out-flow queue as ta+FFTT (free-flow travel time)
If the current simulation time t equals to or is later than ta+FFTT, if the link out capacity is still available, move this vehicle to the next link, otherwise stay in the out-flow queue
Out –flow
Queue
In-flow Queue
Available capacity
at every simulation interval
Item | Corresponding variables
FFTT | link.free_flow_travel_time_in_min
In-flow queue | link.entrance_queue
Out-flow queue | link.exit_queue
Notes: How to Determine Link-In Capacity at Each Simulation Interval
  Free-flow or partially congested  use pre-specified reduced capacity
  Fully congested according to N-Curve formula
    --> Link-out flow rate from the previous simulation interval
How to Determine Link-Out Capacity at Each Simulation Interval
Minimal of the following elements
  Pre-specified Average Capacity
  If a link is fully congested, its link-in capacity will be distributed to incoming links as function of lanes

## Slide 20: Part 2 Introduction to DTA modelling principles
2.1 Dynamic Traffic Assignment Modelling Framework
2.2 Agent-based Routing
2.3 VOT Distribution
2.4 Multiple Traffic Simulation Models

## Slide 21: 2.1 DTA Modelling Framework
Item | Corresponding functions or steps
Link Traversal | step 2.3 in g_traffic_simulation()
Node Transfer | step 2.4 in g_traffic_simulation()
Path processing | Network.optimal_label_correcting( )
User decision | Network. find_path_for_agents()
Notes: In general, the traffic simulation assigns vehicles to different paths based upon link travel time. The physical process of moving vehicles works in a two-step process. First, a vehicle is moved across a link during the link pass, and then moved between links at the node during the node pass. Link travel times from the traffic simulator are fed to the shortest path model for path selection. The new paths are then fed back into the traffic simulator in the next iteration.

## Slide 22
Outflow capacity
Inflow capacity
Storage capacity
Exit Queue
Outflow Capacity
Inflow Capacity
Entrance List
Storage Capacity
Newell’s simplified kinematic wave model
2.4 Multiple Traffic Simulation Models
Item | Corresponding variables
Outflow capacity | Link.td_link_outflow_capacity[]
Entrance List | Link. entrance_queue
Exit Queue | Link. exit_queue

## Slide 23: 2.4 MultipleTraffic Simulation Models
  Inflow capacity = outflow capacity
Outflow Capacity
Inflow Capacity
Queue propagation
Item | Corresponding variables
Outflow capacity | Link.td_link_outflow_capacity[]
Entrance List | Link. entrance_queue
Exit Queue | Link. exit_queue

## Slide 24: 2.4 Multiple Traffic Simulation Models
Node
Node Transfer
Check Outflow Capacity
Check Inflow Capacity
Check Storage Capacity
Node transfer
Item | Corresponding variables or functions
Outflow capacity | Link.td_link_outflow_capacity[]
Node transfer | step 2.4 in g_traffic_simulation()
Entrance List | Link. entrance_queue
Exit Queue | Link. exit_queue
Notes: Going into more specifics, let’s take a closer look at the link pass and node pass. The capacity constraints are enforced at both ends of each link. At the beginning of the link, the entrance list keeps track of vehicles entering the link, enforcing the inflow capacity constraint. During the link pass, the vehicles are moved between the entrance list and the exit queue. The exit queue keeps track of vehicles waiting to leave the link, enforcing the outflow capacity constraint. Vehicles are then moved between the exit queue and the entrance list of the next link during the node.

## Slide 25
  Distribute inflow capacity to upstream links
  Lane & demand-based methods
Node
Available Inflow Capacity
80%
20%
2.4 Multiple Traffic Simulation Models
Merge Models

## Slide 26
  Different conditions by lane
  First-In-First-Out (FIFO) constraint
  Relaxation to prevent extreme bottlenecks
Node
2.4 Multiple Traffic Simulation Models
Diverge Models

## Slide 27
  Effective green time, saturation flow rate, movement-based capacity
  Relaxed inflow constraints
2.4 Multiple Traffic Simulation Models
Signalized Intersections

## Slide 28
  Input: Average hourly capacity, cycle time, offset at node
  Output: Effective green time per cycle(capacity/saturation flow rates)
2.4 Multiple Traffic Simulation Models
Signal Timing & Hourly Capacity